Octel 250

Message Server

Configuration Note 5404 - Ver. C  (3/01)

ROLM CBX 8000/9000/9751

1.0  method of integration

The FLT-R emulates Rolmphone 400 digital telephone sets

The digital set emulation integration on the Rolm CBX, the FLT-R, appears as one or more digital Rolmphone 400 telephone sets to the PBX.  When a call is presented to FLT-R ports, the display information is read and the call is then answered with the appropriate greeting. Message-Waiting is set using the Message Center function over dedicated FLT-R Port(s).

Octel 250 requirements

2.0  octel ordering information

FLT-R(s) - Each FLT-R supports 8 Ports

Set Emulation Software feature (Feature Bit 33)

RS232 Integration feature (Feature bit 34)

In-band Integration feature (Feature bit 35)

PBX hardware requirements

3.0  PBX HARDWARE requirements

Rolmphone Interface channels, One per FLT-R port

One analog line for remote service access (RDAC)

25-pair, male Amphenol cables, one per FLT-R

PBX software requirements

3.1  PBX SOFTWARE REQUIREMENTS

Supported software:  Release 9005 and below

Supported integration features

4.0  SUPPORTED FEATURES

Station forward to personal greeting
- all calls
- DND

System forward to personal greeting
- Busy
- RNA							                 - DND

Message-waiting Indicator
- lights
- audible message waiting (stutter dial tone)

Automated attendant						   - Supervised							   - Unsupervised

Outcalling

Multiple return-to-operator

Direct call

Personal greeting of original-called party on double-call forward

Reply to message left by subscriber in internal telephone-answering mode

Call sender

Multiple Personal Greetings					      - RNA								           - Busy

Configuring the ROLM 8000

5.0  ROLM CBX 8000 configuration

(	Define the extensions that connect to the Octel ports using the following commands:

NEX extn#

(	Using the SCS command, assign a class of service (COS) to each of 	these extensions.  The COS must have the following feature:

NOH - No Howler Tone if left off hook (feature 17)

The COS must not have the following features:

NFL - No Flash Allowed (feature 13)

APK - Automatic Camp-On (feature 15)

UNV - Unavailable (feature 18)

TER - Terminate Only (feature 24)

(	Configure the Rolmphone Interface ports connecting to the FLT-R. Using the RFC command, create a Rolmphone 400 feature table as shown in Table 1.  The button placement must be exactly as specified, or the FLT-R will not function properly.

NOTE: Make sure to configure the feature table with the MWCTR key, not the MSGWT key.  MWCTR enables the RPI channel to set and cancel message waiting at subscribers' phones. ROLMPhone 400 feature table programming for the FLT-R

Table 1. Rolmphone 400 Feature Table

(	Assign the ROLMphone 400 feature table to the first RPI channel:

REC			“Revise ETS configuration” 
				command

XXYYZZ		Enter the physical address (PAD)
				of the first RPI channel

#			Enter the feature table number created in the 					previous step for the FLT-R ports

EXTN#		Leave this entry blank

TYPE		Enter 'RP400'

(	Repeat the REC command for all the remaining RPI channel, 	changing only the physical address (PAD) entry to correspond to the 	proper RPI port

(	Assign a display module to the RPI channels connecting to the FLT-R:

ROM		“Revise Rolmphone option
				 modules” command

PAD			Enter the physical address of the 						RPI channel

FLAG		Enter '1' to set the display module

FLAG		Enter '0' to set no speakerphone 							module

FLAG		Enter '0' to set as a RP400, not a CAS 						console

(	Repeat the ROM command for the remaining RPI channels, changing 	only the PAD entry to correspond to the proper RPI port.

(	The following programming assigns the extensions to the RP400.

RKB		“Revise Key Button” command

PAD		Enter the physical address of the RPI channel used

BT#		1

EXTN#	Enter the extension number to be
			assigned to the line number

FLAG	1

FLAG	0

FLAG	0

(	Repeat the RKB command for all remaining RPI channel connecting 	to FLT-R 	ports.

(	Assign all the newly-created Rolmphone interface channels, except 	for the channel(s) to be used as dedicated message waiting ports, to a  	Hunt/Distribution Group using the RHG command.  The pilot number 	of this Hunt/Distribution group is the Octel access number 	subscribers call to access the Octel 250.  This is also the pilot number 	that subscribers will use as the forwarding target for their extensions.

Configuring the Rolm CBX 9000/9751

5.1  rolm cbx 9000/9751 configuration

(	The CBX must have the Internal Dial Tone parameter set to HIGH 	frequency, not LOW frequency. Otherwise, the Octel 250 will not 	recognize dial tone.  LOW frequency is the default value.

(	Define the extension numbers that will connect to the Octel 250 	ports using the CR EXT command.

(	Assign a class of service (COS) to each of these extensions.  The 	COS must have the following feature:

NOH - No Howler Tone if left off hook

The COS must not have the following features:

NFL - No Flash Allowed

ACB - Automatic Camp-On

APV - Always in Privacy

TRM - Terminating Only

Configuring the digital ports

(	Create a Rolmphone 400 feature table as shown in Table 2.  The button placement must be exactly as specified, or the FLT-R will not function properly.

NOTE: Make sure to configure the feature table with the MWCTR key, not the MSGWT key.  MWCTR enables the RPI channel to set and cancel message waiting at subscribers' phones. ROLMPhone 400 feature table programming for the FLT-R

Table 2. Rolmphone 400 Feature Table

(	Using the CR RPI/RLI command, configure the Rolmphone Interface 	channels connecting to the FLT-R ports.  Note the following:

TYPE 		RP400

TBL NO.		The number of the feature
				table created in the previous
				step

RING			Yes

MW			No

BI			No

CLD NAME		No

(	Configure the remaining Rolmphone channels to be connected to the 	FLT-R ports.

(	Assign all the newly-created Rolmphone interface channels, except 	for the channel(s) to be used as dedicated message waiting ports, to a  	Hunt/Distribution Group using the CR HD_G command.  The pilot 	number of this Hunt/Distribution group is the Octel access number 	subscribers call to access the Octel 250.  This is also the pilot number 	that subscribers will use as the forwarding target for their extensions.

NOTE:  The Rolm CBX allows up to 50 members in a Hunt/Distribution Group.  If the Octel 250 is equipped with more than 50 integrated ports, simply configure a second Hunt/Distribution Group, assigning the remaining ports to it.  Then, assign the pilot number of this second Hunt/Distribution Group as the forwarding target for the Octel access hunt group.  This is done within the HD_G screen , by configuring the following fields:

FWD/BUSY       C (condition)          B (both internal and external calls)

NUMBER               Enter the second Hunt/Distribution 						       Group pilot number.

Configuring the Octel 250

6.0  Configuring the Octel 250

(	Menu 1.1  -  System Parameters

Type of Switch connected to:  B - PBX Integration Device / ROLM

Number of Digits in Extension used for Outcalling and ECP:

Number of Digits in Extension used for Message Waiting:

Sender ID Used for Telephone Answering Messages:  2 - Calling Party, if known

Menu 4.1  -  Port Configuration

Extension/Phone No: Enter the extension number of the digital line

Line Type: 146 (ROLM 9005 and below)

Message Waiting: N for all call processing ports, and Yes for the dedicated message waiting port(s).

(	Menu 6.1 -Transfer Dialing Sequences

“Flash” On-hook Time: set to average of the minimum and maximum values configured on the ROLM - Typically 700ms

“Pause” Time: 1000 ms

Dialing Sequence to Transfer a Call: Leave Blank

Dialing Sequence to Reconnect a Call -

Ring/No Answer:  Leave Blank

Busy:  Leave Blank

(	Menu 6.2 - In-band Integration

Leave all values to default settings.  This menu is not used by this integration.

(	Menu 8/9.1  -  Subscriber Mailbox Profile

Subscribers Extension:  Enter extension number assigned to subscriber’s telephone set.

Message Waiting Allowed: Y only for mailboxes associated with subscribers' telephones that have message waiting enabled.  N for mailboxes not associated with subscribers' telephones.

Int. Link Number: Not Used

7.0  CONNECTING THE FLT-R

Connecting the FLT-R

(	Each FLT-R supports eight digital voice ports. Each FLT-R connects 	to the switch via a single 25 pair male amphenol connector cable. The 	first 	port uses the first pair of the cable, every other pair is used by 	the remaining ports.

7.2  Testing the Installation

Testing the installation

(	Create two mailboxes associated with two test extensions. Record a 	name and personal greeting for each mailbox.

(	Make sure these extensions have been forwarded under busy and no-	answer conditions to the Octel 250 pilot number.

(	Using one test extension, call the other test extension. You should 	hear the personal greeting.

(	Leave a message. Verify that the message waiting indicator turns on.

(	Verify that return-to-operator works properly.

(	Call the Octel 250 from a test extension. You should 	immediately hear the recorded name and be asked to enter your 	password.

(	Review the message in the mailbox. Verify that you can 	automatically reply to internal telephone-answering messages.

8.0  CONSIDERATIONS

Important notes regarding this integration

8.1	The following six patches are required on the ROLM 9751 Satellite Operations can be tailored to meet customer needs. The following features are supported for subscribers on the remote CBX:
-	Forward to personal greeting
- 	Return to operator on the local CBX only
- 	Direct call 
- 	Message waiting through outcalling

See section 9.0 of this note for further information.

8.2	The ROLM CBX does not allow a call to be transferred unsupervised to an extension that is busy and not busy forwarded. This is to prevent a caller from being transferred to a busy signal. Instead, the call will be sent back to the extension of the person attempting to transfer the call.

This will affect return to operator and unsupervised automated attendant transfers. Make sure any extensions to be used as attendants or any extensions that can be dialed from an unsupervised automated attendant mailbox have busy forwarding targets programmed. Otherwise, callers might be returned to the Octel 250 when attempting to transfer out of it.

Avaya OMD recommends using dedicated message waiting ports.  Although this is not an absolute requirement, if dedicated message waiting ports are not used, subscribers may experience long delays with message waiting indication during high-traffic periods.

When integrating with redundant ROLM CBX’s, the O250 will log 	F9 errors in the status log during switchover.  Redundant ROLM CBX’s are normally configured to perform a periodical “switchover”, usually to occur daily at midnight. When a switchover occurs, the O250 will log two F9 entries in the status log for every FLT-R port connected to the switch.  One F9 entry is logged when the O250 first detects the momentary loss of digital signal;  the other F9 entry is logged as soon as the digital signal is detected once more.  Depending on the system size, this can cause the status log to overflow with F9 errors.

9.0  Addendum A - Satellite Operations Software

One Octel 250 can support two or more Rolm CBX’s, provided that all switches have Satellite Operations software and all remote systems have Off-Premise Forwarding (Off-system Station Forwarding). The Octel 250 must be integrated and located at the main CBX. Use the following procedure referencing the diagram below.

One hunt group (with no members) per remote subscriber must be created at both the remote and the main site. At the remote CBX, the hunt-group pilot number must be off-system station forwarded to the hunt-group pilot number at the main site using the “Invoke Call Forward” command (a Control of Station Features (CSF) command). The hunt-group pilot number at the main site must system forward on a busy condition to the Octel 250 pilot number. A transfer mailbox should be created for each remote subscriber that matches the pilot number of the subscriber’s hunt group at the main site. This transfer mailbox should have as its “Transfer Mailbox Number” the subscriber’s mailbox number. With the use of transfer mailboxes, remote subscribers’ mailbox numbers will match their extension numbers. To forward their stations to personal greeting, subscribers system or station forward their extensions to their own individual hunt group at the remote site.

Message Waiting Notification at the remote CBXs will only be possible through outcalling. Return to operator is possible only to the main CBX site. This process prevents callers from being sent back to the Octel 250 (system greeting) when all tie trunks are busy. In addition, the ROLM CBX does not allow a blind transfer across the tie trunks.

NOTE: This procedure uses a large number of hunt groups (for phantom extensions) in the main and remote CBX(s). If a remote CBX has a large number of extensions, this might not be practical. It might be better to utilize two Octel 250 platforms.

NOTE: The remote or main CBX may be a CBX II 8000 or CBX II 9000. Lexes (logical, or phantom, extensions) should be used on the CBX II 8000 in place of hunt groups.

©2002 AVAYA Inc. All rights reserved. All trademarks identified by the ®, SM and TM are registered trademarks, servicemarks or trademarks respectively. All other trademarks are properties of their respective owners. The above information is based on knowledge available at the time of publication and is subject to change without notice. Printed in U.S.A.

AVAYA

911 Murphy Ranch Road

Milpitas, CA 95035-7912

(408) 577-7000

http://www.avaya.com