Avaya BCM Solutions Test Lab

Business Communication Manager BCM 50 and BCM450 Release 6.0 Configuration Guide for Skype SIP Connect Service

Issue 1.1

Abstract

This document provides guidelines for configuring a SIP Trunk between a BCM50 or BCM450 Release 6.0 and Skype SIP Connect Service

Table of Contents

Table of Contents	2

1.0 Introduction	3

1.1 Document Change History	3

2.0 System Software / Loadware	4

3.0 Features	5

3.1 Features Supported	5

3.2 Technical Caveats	5

4.0 Overview	6

5.0 System Configuration	7

5.1 BCM Configuration	7

5.1.1 IP Trunks Settings Configuration	7

5.1.2 SIP Media Parameters Configuration	7

5.1.3 Importing Skype Template to BCM	7

5.1.4 Create Public SIP Trunk Accounts	8

5.1.5 Customize the Account	8

5.2 Dialing Plan	9

5.2.1 Line Pool Configuration	9

5.2.2 Dial Plan Configuration	9

5.2.3 SIP Trunk Routing table Configuration	10

5.2.4 Configuring Incoming Calls from SKYPE to BCM	11

5.2.5 Giving Access to SIP Trunks	12

# Introduction

This document is intended to provide information to installers configuring a BCM50 or a BCM450 Release 6.0 for SIP trunk inter-working with Skype. The information provided is specific for the SIP trunk inter-working, unrelated configuration is not considered within this guide. This document assumes that the installer has undergone Avaya approved BCM training and has a working knowledge of BCM installations.

## Document Change History

| Date Version | Summary of Changes |
| --- | --- |
| July 23, 2010 0.1 | Original publication |
| October 1, 2010 1.0 | Release |
| February 14, 2011 1.1 | Template attached |

# System Software / Loadware

To achieve successful interoperability between the BCM and Skype SIP Trunking, the various network elements must be running the version of software as shown below:

| System | Platform | Firmware |
| --- | --- | --- |
| BCM 50 | All platforms | Release 6.0 GA build 1.02. |
| BCM450 | All platforms | Release 6.0 GA build 1.02. |
| BCM Phones | All supported phones | As provided by release 6.0 GA build 1.02. |

Table 1 Validated Equipment and Software

# Features

## Features Supported

- The following are capabilities tested and validated:

- Basic calls (G711 a-law/u-law and G729 both with 20ms packetization)

- Calling line (number) identification presentation

- Calling line (number) presentation restriction

- DTMF (RFC 2833)

- Call hold

- Call transfer (attended and unattended)

- Conference calls

- Call forward

- Call waiting

## Technical Caveats

- FAX is not supported by Skype.

- The Windows Skype client version 4.2.0.158 displays ‘Failed Call’ when calling a BCM set that is busy.

- Skype does not support Early Media in SIP.

- Calls from Skype users appear on BCM as ‘Private Number’ in the following cases:

  - Skype user does not have an Online Number

  - Skype User does not have a configured Caller ID

# Overview

Figure 4-1 shows a typical deployment of a SIP trunk between BCM R6 and Skype. In the deployment, a SIP unaware layer 3 device with NAT and firewall is deployed between the BCM and Skype. The IP address assigned to the BCM and all IP phones is private and since Skype does not support remote NAT compensation, the BCM is configured to compensate for the presence of the local NAT.

Figure 4-1 SIP Trunking between BCM and Skype

# System Configuration

This section provides procedures for configuring a SIP trunk on BCM Rls. 6.0 to Skype.

## BCM Configuration

In order to configure a SIP trunk between BCM and Skype, do the following:

### IP Trunks Settings Configuration

- Navigate to  Configuration ( Resources ( IP Trunks( General

- Click on the “IP Trunks Settings” tab

- Ignore in-band DTMF in RTP: by clicking on the check box next to it.

### SIP Media Parameters Configuration

- Navigate to Configuration ( Resources ( IP Trunks( SIP Trunking

- Select the Media Parameters tab.

- In the Preferred Codecs section, configure G.729, G.711-uLaw as the first and second preferred codec respectively.

- In the codec Settings section,

- In the codec Settings section, select 20ms as the payload size for both G.729 and G.711

- FAX is not supported by Skype.

- Provide in-band ringback must be left unchecked.

### Importing Skype Template to BCM

- Navigate to  Configuration ( Resources ( IP Trunks( SIP Trunking

- Select the Public tab.

- Select the ITSP Templates tab

- Save the template file below to your computer.

- Click on the Import button

- Select Yes to acknowledge the warning

- An Import Files dialog box will open

- Click on Browse and navigate to the directory containing the Skype templates

- Select the Skype template and click on Select Files

- Click the OK button to import the template to the BCM

### Create Public SIP Trunk Accounts

- Navigate to  Configuration ( Resources ( IP Trunks( SIP Trunking

- Select the Public tab.

- Next select the Accounts tab.

- Click on the Add button.

- In the Add Account dialog box that pops up, click on Select Template.

- In the Choose Template dialog box, choose one of the Skype templates and click on the Select button.

- In the Add Account dialog box that opens up

  - Provide a unique name for this account in the Name field

  - Provide a descriptive name for this account in the Description field

  - Enter the Skype user id in the SIP Username field.

  - Enter the Skype user id in the Auth name field.

  - Enter the Skype user password in the Auth password field.

  - Leave the rest of the parameters at their default values.

- Click on the OK button

### Customize the Account

- Navigate to  Configuration ( Resources ( IP Trunks( SIP Trunking

- Select the Public tab

- Next select the Accounts tab

- Select the Skype account

- The Details of the Accounts appears at the bottom

- Select the User Accounts tab in the Details of the Accounts table.

- Select the first row in the User Accounts table.

- Click on the Modify button and this should open the Modify Account dialog box.

- In the Modify Account dialog box:

- Provide a description for this user account in the Description field

- Set the CLID value equal to CLID of the BCM set, which is a concatenation of Public Network Code and Public OLI. The Public network code is configured in 5.2.2.

- Within the Message Handling section;

  - Set the CLID Override value to a Skype user id.

  - Set the PAI CLID Override to the same value as the CLID Override.

  - Click the OK button

- Navigate to Configuration ( Telephony(Global Settings(Feature Settings

- Provide a name in the Business Names section

- Navigate to Configuration ( Telephony( Sets(Active Sets

- For each active set in the Active sets table, change the Name column to name of user of that BCM phone.

- For each active set in the Active sets table, cconfigure the Pub OLI. CLID for outgoing calls from the set is constructed as: Public network code + Pub. OLI . The Public network code is configured in 5.2.2.

### Caller ID Delivery for Outgoing Calls with Skype

Skype Connect uses the following mechanism to deliver Calling Line ID on outgoing PBX calls:

Skype Connect allows a PBX to select the outbound caller ID on a call by call basis using

RFC3325 P-Asserted-ID and Privacy:id headers.

Skype Connect llows a business to register their landline DDI’s with their SIP profile, the

maximum number of landline numbers that can be registered is 99. In order for a business to

register their landlines they must have passed our company verification process that can be

located in the BCP under account details. The landline numbers must belong to the business and

must be located in the same country as the business is registered.

When a business has been verified, any landline number that is registered is inserted into a

virtual CLI database that also contains all Online numbers associated to the SIP profile. When

the SIP PBX uses the P-Asserted-ID header, Skype check’s the content of the P-Asserted-ID

header against the users CLI database, if the value’s match Skype will then use the number in

the P-ID header as the outbound caller id. If the number does not match, Skype will set the

outbound caller id as anonymous.

In order to control CallerID for outgoing calls via Skype Connect BCM administrator has to use SIP trunk user account PAI CLID Override field. The field can be set to the desired CallerID provided the CallerID is registered via Skype Manager as described above.

If a single SIP trunk user account is used for Skype ITSP Account only a single CLID can be specified for all calls from any extension on the BCM. If there is a need to set the CLID on a per-extension basis or for a group of BCM extensions multiple SIP trunk user accounts have to be created at the Skype ITSP account level.

Each SIP trunk user account is keyed by CLID field. In order for a BCM extension to be associated with a SIP trunk user account the CLID has to match the caller Public OLI (prefixed by Public Network Code Configuration ( Telephony(Dialing Plan->Public Network->Public Network Settings).

If multiple SIP trunk User Accounts are associated with the same Skype SIP profile, SIP registration can only be turned on for one of the SIP trunk user accounts associated with the same Skype SIP Profile. SIP Trunk User Accounts are associated with Skype SIP profiles by way of using SIP User credentials of the Skype SIP Profile.

BCM Outgoing Name and Number (ONN) Blocking feature (F819) is compatible with Skype Connect and can be used to block ONN on a call-by-call basis.

## Dialing Plan

### Line Pool Configuration

- Under Configuration ( Telephony ( Dialing Plan; select Line Pools.

- Select BlocA.

- Click on the “Add” button to add DNs of sets that need to access the above line pool.

### Dial Plan Configuration

- Under Configuration ( Telephony ( Dialing Plan ( Public Network, define the Public Received number length. Check with Skype for the appropriate value.

- Set the Public Network Dialing Plan to Public (Unknown)

- Set the Public network code which is a Caller ID prefix for example 613763

- In the Public Network DN Lengths table, configure the DN prefixes and their corresponding lengths.

- Under Configuration ( Telephony ( Dialing Plan ( Routing, and select the Routes tab

- Add a route by clicking on the Add button.

- In the Add Route dialog box, provide an unused route and click on the OK button. This is the preferred route.

- The Dialing Plan – Routing table will be displayed.

- Click on the route just created

- Under the External Number column of the newly created route, insert a number that will appended to the dialed number and presented to the SIP trunking module on the BCM for routing. This number will be stripped off before routing the call to Skype.

- Under the Use Pool column of the newly created route, double click to select BlocA from the drop down list.

- Under the DN Type column of the newly created route, double click to select Public (Unknown) from the drop down list.

- Repeat Steps 6 to 11  to add a backup route. This route will be used if the attempt to route the call via the preferred route fails. In the External Number column for this secondary route, provide a number which is different from that used in Step 10..

- Click on the Destination Codes tab.

- Configure a destination code to route dialed digits by clicking on the Add button. Digits that begin with this destination code will be presented to the SIP trunking component on the BCM for routing towards the Service Provider.

- In the Add Destination Code dialog box, enter a numeric number for the destination code and click on the OK button.

- Select the row representing the Destination Code entered in the previous step

- Under Normal Route column, double click and enter the route entered in Step 7.

- Under the Absorbed Length column, specify the number of digits that will be absorbed before pre-pending the configured External number configured in Step 10 and sending the rest of the digits to the SIP trunking component.

- While the row representing the Destination Code enter in Step 16 is selected, in the Alternate Routes table that shows up below, click on an unused schedule

- In the Second Route column of the selected row above, provide the route configure in Step 13.

- Navigate to Configuration( Telephony(Scheduled Services

- Click on the schedule used in Step 20 above.

- Define the times when this schedule will be active by providing the start and stop times for each day of the week.

- In the Services section that appears below, select the schedule used in previous steps and do the following:

- Double click the Routing Svc column and select Auto to active the schedule.

- Enable overflow by putting a check in the Overflow checkbox

### SIP Trunk Routing table Configuration

- Navigate to Configuration ( Resources ( IP Trunks( SIP Trunking

- Select the Public tab

- Click on the Accounts tab

- Select the first Skype account

- In the Details for Accounts table below, in the drop down list next to Called Number Characters to absorb select the number of digits that will be absorbed by the SIP trunking component before sending the dialed digits to Skype. The number selected here should be the number digits in the External Number configured in Step 10

- Click on the Routing Table tab

- Click on the Add button

- In the Add Route dialog box;

- Provide a descriptive name for the new route in the Name.

- Set the Destination Digits to the value provide as the External Number in Step 10 of section 5.2.2

- In the ITSP Account drop down list, select the Skype account

- Click OK

### Configuring Incoming Calls from SKYPE to BCM

This can be done in one of two ways;

- The DID assigned to the BCM can be associated with a target line assigned to a group of set(s) and all calls to the DID will be routed those set(s).

- All calls to the DID assigned to the BCM can be answered by the Auto Attendant (AA) and from there, a DN can be entered to reach a phone on the BCM

#### Assigning DID to BCM Phones for Incoming Call

- Navigate to Configuration( Telephony( Lines ( Target Line and click on an unused target line

- On the selected Target Line, set the “Pub. Received #” to the last 4-digis of the Skype assigned DID.

- Assign the DN of phones on the BCM that require an appearance on this target line. This will be the phones that will be alerted when call to the Skype assign DID is received.

  - Navigate to Configuration( Telephony( Lines ( Target Line and click on the Target Line configured in Step 2 above

  - Click on the Assigned DNs tab

  - Click the Add button to add the DN of set(s) to this Target Line.

#### Configuring AA to Answer Incoming Calls

Alternatively, the AA on the BCM can be configured to answer incoming calls and then call routed to a target phone on the BCM by entering the extension of the set at the AA prompt. To do this,

- Navigate to Configuration( Telephony( Lines ( Target Line and click on an unused target line

- On the selected Target Line, set the “Pub. Received #” to the last 4-digis of the Skype assigned DID.

- Navigate to Configuration(Application(Voice Messaging/Contact Center

- Click on the Launch CallPilot Manager.

- This launches a web browser to the BCM. Log in with the administrator credentials

- On the left hand navigation menu, click on Auto Attendant

- In the Line Administration web page, scroll down to the Target Line configured in Step 1.

- Under the Command Column, click Change

- In the Line Properties web page, select Auto-Attendant as the Answer Mode

- Click the Submit button.

### Giving Access to SIP Trunks

To give access to BCM phones to make outgoing calls across the SIP trunk;

- Navigate to Configuration(Telephony(Sets(Active Sets

- Click on the Line Access tab

- Click on the DN of each the registered BCM phones in turn and click on the Line Pool Access tab

- Click on the Add button

- In the Add Line Pool dialog box, type blocA

- Click OK

- Repeat steps 3 to 6 for each of active sets on the BCM.

©2010 Avaya Inc. All Rights Reserved. Avaya and the Avaya Logo are trademarks of Avaya Inc. All trademarks identified by ® and ™ are registered trademarks or trademarks, respectively, of Avaya Inc. Nortel, Nortel Networks, the Nortel logo, and the Globemark are trademarks of Nortel Networks. All other trademarks are the property of their respective owners. The information provided in these Application Notes is subject to change without notice. The configurations, technical data, and recommendations provided in these Application Notes are believed to be accurate and dependable, but are presented without express or implied warranty. Users are responsible for their application of any products specified in these Application Notes. If you have any issues with the solution described in this document, please contact 1-800-4-NORTEL

# Text boxes

Public Internet

PSTN

BCM

SMB network protected by a NAT/FW

with BCM on the LAN

NAT/FW

Skype

Local NAT

Compensation

Skype SIP Trunk

Phone

A

B

C

Phone

D

TDM Phone