Configuration Note 77115

Iwatsu ZTD *

Revised 1/31/00

1.0	method of integration

Inband signaling is used for integration

Inband signaling is used for integration.  Call forward to personal greeting is achieved via DTMF signals passed from the Iwatsu ZTD to the Octel 50 family of products.  Message waiting indicators are set and canceled by dialing a feature access code followed by the extension number.  A hook-flash followed by the extension transfers the caller to the operator.

1.1 Supported Voice Processing Module

Supported Voice Processing Module

The Octel 50 is a Year 2000 (Y2K) compliant, PC based, enhanced voice messaging product release intended to replace the Smooth Operator, Smooth Operator Lite and Cooperator product lines.

2.0	ORDERING INFORMATION

Ordering Information

Octel 50 integration will support 16ports.

This integration supports up to 16 Octel 50 ports.  For installed systems that have port capacities above 16 ports contact your CAG representative for the proper solution.

Voice Boards supported:

Dialogic DIALOG/4 ™

Optional Fax Boards supported:

Brooktrout TR114 Series Universal Port™

Optional Remote Service

External Modem

3.0	Switch HARDWARE REQUIREMENTS

Switch hardware requirements

MCPU W-1 CPU 4.5 or 5.0

Single Line Subscriber Card (SLSB8)

DTMF receiver circuit card (RECV8-1)

RNGU Ring Generator

3.1	Switch SOFTWARE REQUIREMENTS

Switch software requirements

• Version 4.5 to 6.0

3.2	Additional Material Requirements

Additional Material Requirements

The voice board used to interface Octel 50 VoiceMail is a four-port board.  System configurations may reflect partial use of a board.  The board used to interface Octel 50 FaxMail is a two-port board.  You will need:

One RJ-14 jack with 4-conductor line cord for every two Octel 50 ports.

For optional remote service access:

One analog line

One RJ-11 Jack for above and 2-conductor modular telephone cord.

If  optional FaxMail is installed:

One analog line per fax port

One RJ-11 jack for every Brooktrout TR114 fax port

4.0	SUPPORTED FEATURES

Supported integration features

[(] Items are supported

| System Forward to Personal Greeting |
| --- |
| Message Waiting |
| All Calls | [(] |
| LCD Display | [ ] |
|  | Ring/no answer | [(] |
| LED | [ ] |
|  | Busy | [ ] |
| Lamp | [(] |
|  | Busy/No Answer | [(] |
| Audible / Stutter Dial Tone | [ ] |
|  | Do Not Disturb | [ ] | Multiple Return to Operator | [(] |
| Station Forward to Personal Greeting |
| Direct Call | [(] |
|  | All Calls | [ ] | Auto Attendant | [(] |
|  | Ring/no answer | [ ] | Outcalling | [(] |
|  | Busy | [ ] | Personal Greeting of Original-Called Party |
| Busy/No Answer1 | [(] |
| Multiple Call Forward | [(] |
|  | Do Not Disturb | [ ] |
| Double Call Forward | [ ] |
| Flexible Forwarding |
|  | Call Coverage | [ ] |
|  | Forward to No Answer Greeting | [ ] | Intercom Paging | [ ] |
|  | Forward to Busy Greeting | [ ] | Supervised Transfers2 |
| Intercom/CO Forwarding | [ ] |
| Call Screening | [(] |
| Call Queuing | [(] |
|  | Intercom Paging | [(] |
|  | Record Telephone Conversation | [ ] |
| Notes: 1System Forward to Personal Greeting (Call Coverage) via Fixed Call Forward |
| 2See Section 7.3 |

4.1	disconnect type

Disconnect is achieved by a hang-up string sent from the PBX. For proper external disconnect supervision, Ground start trunks or Supervised loop start CO lines are recommended.  See section 6.0

5.0	Configuring the Iwatsu ZTD

Configuring switch system parameters

Before you begin programming, it is recommended that a hard copy of the customer database be obtained to verify existing programming.

Configuring Octel 50 Ports

5.1	Configuring the ztd for voice mail

Refer to the Programming section in the Iwatsu ZTD manual for information on entering, saving and exiting database programming.

The Iwatsu ZTD system allows to install the AAVM ports to EXTs. 144 through 151, and can only have 6 AAVM ports total.

The Octel 50 extension numbers must either be set as line appearances on the phone or programmed to a Floating CO group to allow transfers to the operator.  (See Note: section 7.6)

Program 	03  Station Type Assignment	
		Program  Octel 50 Ports to be AAVM

Program	12  DTMF Receiver Assignment
		DTMF Receiver Assignment should be 8,0

All references to Octel 50 pertain to the entire family of products

Program	16  Operator Camp-on Recall
		Must be higher than Program 87 Call Forward No Answer timer

Program  17  Station Camp-on Recall
		Must be set to a higher value than the Call Forward No Answer 		timer  (Program 87) but a lower value than the Operator Camp-on 		Recall timer (Program 16)

Program  50  CO Disconnect Signal Detect
		Set CO Disconnect for every line key

Program  56  Voice Mail Line
		Voice Mail line should be ON for all Octel 50 ports

Program  87  Call Forward No Answer timer
		Set the Call Forward No Answer timer to 12 - 15 Seconds.

Program  91 - 04  Fixed Call Forwarding (Busy / No Answer) to VM
		Set Fixed Call Forwarding on subscriber extensions as needed

Program  91 - 20  VM DTMF Duration Time
		Set VM DTMF Duration to 15 (150 ms)

Program  91 - 21  VM Pause Timers
		Set to 00 if using DSS programming (unused in PC programming)

Program  91 - 22  VM Packet Table
		Set Packets 4 through 12 to 7 for Forwarding to VM
		Set Packet 13 to 8 for Direct Call
		Set Packet 19 to 55** for Disconnect Packet

Note:	All of the Forwarding, Direct Call and Disconnect  packets are programmable, we recommend 7 for Forwarding (packets91-4 through 91-12), 8 for Direct Dial (packet 91-13) and 55** for the Disconnect (packet 91-19). The integrator module reflects these recommendations.

5.2	Assigning Octel 50 extensions to hunt group

Assigning Extensions to Hunt Group

Assign the Octel 50 ports to AAVM in Program 03 Station Type Assignment.  The Iwatsu ZTD will automatically put the AAVM stations in Hunt Group 54.

Programming Subscriber Stations

5.3	Programming Subscriber Stations

Program	78  Flexible Key Assignment
		Select the key you wish to program as a Message Waiting Light. 		Program the key as MSG.

All references to Octel 50 pertain to the entire family of products

If no Flexible Key Assignment is set for Message Waiting Lights, the FEAT key will be lit when a message is present in the subscribers mailbox. (If the FEAT key is used as a MWL instead of a Flexible Key Assignment you must press 6 to log into your mailbox to retrieve messages).

5.4	STATION Forward To Voice Mail

To manually forward a phone to Voice Mail:

Key stations: With the handset off hook, press [FEAT] [FWD]. Dial 54 (the hunt group number) plus the code for the desired forwarding.

# = NA Call Forward
0 = All Call Forward
* = Busy / NA Call Forward

To forward a Key station on Busy/NA:

Lift handset, press [FEAT] [FWD] then dial 54* and hang up.

Octel 50 programming

6.0	Configuring the Octel 50

During the install process, run the Integrator program and choose the 
Iwatsu ZTD.  The Integrator will place appropriate feature codes into the Octel 50 Setup.

The following codes should be inserted by the integrator.  Three digit extensions are assumed.

| Outside Line Access Code | 91, Note: Section 7.4 |
| --- | --- |
| Off Hook Delay (OFFHDLY) | 25 |
| Hook Flash Interval (FLINTVL) | 50 |
| DTMF Tone Length (TONELEN) | 8 |

Transfer, Paging and Screening Parameters

| Custom Transfer Code | &,XDR |
| --- | --- |
| Intercom Paging Code | &,C280N |
| Call Screening Release Code When Transfer | &, |
| Release Code for Intercom Paging | &, |

Message Waiting Parameters

| Permit Message Waiting Lights | Enabled |
| --- | --- |
| Message Waiting Light Prefix ON | 1*1 |
| Message Waiting Light Prefix OFF | 1*0 |
| Light Message Waiting Light for Every Message | Enabled |

Hangup Detection Parameters

| Hangup String (HANGUPSTR) | 55** |
| --- | --- |
| Hangup String Timeout (HANGUPDLY) | 100 |

Inband Parameters

| Total Number of DID Digits | 4 |
| --- | --- |
| DID Terminating Character | (blank) |
| Seconds to Wait for DID | 1 |
| Location of Inband Signaling Code | 1 |
| Number of Milliseconds to Wait for Digits | 750 |
|  | Code for Go to Voice Mail | 7 |
| Start at End of String for Go to Voice Mail | Enabled |
| Location of Mailbox Number for Go to Voice Mail | 3 |
|  | Code for Immediate Subscriber Login to Mailbox | 8 |
| Start at End of String for Immediate Login | Enabled |
| Location of Mailbox Number for Immediate Login | 3 |
|  | Start at End of String for Default Code | Enabled |
| Location of Mailbox Number for Default Code | 3 |

Note:  Verify these dialing sequences for your PBX

Important notes concerning this integration

7.0	CONSIDERATIONS/ALTERNATIVES

The following items should be considered, below:

Station Programming

Call Analysis Programming

Supervised Transfers

Outbound Calls

Multiple Call Forward

Floating CO Groups

7.1	Station Programming considerations

Do not set DND forward to VM from a station set.  If this forward option is used the caller will not go to voice mail.  Use forward All Calls instead.

7.2	Call Analysis Programming considerations

Call Analysis (CCA) must be run manually to a station.  To run CCA manually set Channel IN to 0, leave Channel OUT as it is, enter a physical extension number in the Phone Number field.  It is best to use the extension of a phone that is next to you as you will be asked to make the phone busy, let the phone ring and answer the phone etc.  Make sure the extension you are using does not have hands free announce or any type of call forwarding active.

7.3	Supervised Transfer Considerations

If the Octel 50 is programmed to execute a supervised transfer, Handsfree Announce must be disabled.

The Iwatsu ZTD only allows up to 6 ports to be programmed for Voice Mail.  If there is heavy traffic or if Call Queing is used on the system, it may tend to ‘bog down.’

Also it has been noticed that on some systems the prompts, such as “I’m sorry there is no answer at that extension…", tend to get the first words clipped off.

7.4	OUTBOUND Call Considerations

All references to Octel 50 pertain to the entire family of products

The Code to access an outside line in Octel 50 setup must include the Floating CO Group Assignment number from the Iwatsu programming.  The Floating CO Group numbers can be 1 thru 9, the default is 1; this would make the Octel 50 code to access an outside line 91,

7.5	Multiple call forward

Personal greeting of original called party on double or multiple call forward is not available on the Iwatsu ZTD.

7.6	floating co group

If you do not wish to assign the Octel 50 extensions as line appearances on the phone you must use Program 29 to assign them to a Floating CO hunt group.  If neither the line appearance nor the Floating CO hunt is used the caller will not be able to press 0, from the personal greeting, to be transferred to the operator.

*Trademark of Iwatsu America, Inc.

DIALOG/4 ™ is a registered trademark of Dialogic Corporation 
Brooktrout TR114 Series Universal Port™ registered trademark of Brooktrout Technology ™ A BROOKTROUT COMPANY

© Copyright 1995 - 2000 Octel Communications Corporation, a subsidiary of Lucent Technologies Inc.  All rights reserved.  All trademarks identified by the ® and ™ are registered trademarks or trademarks respectively of Octel Communications Corporation, a subsidiary of Lucent Technologies.  All other trademarks are the properties of their respective owners.  The above information is based on knowledge available at the time of publication and is subject to change without notice.

Printed in the United States

Lucent Technologies Inc.
1001 Murphy Ranch Road
Milpitas, CA 95035-7912

1-800-444-5590

Www.lucent.com/Octel

Lucent Technologies, USA 	+408 324-2000
Lucent Technologies, Canada 	+1 416 730-8700
Lucent Technologies, Europe, Middle East, Africa 	     +44 (0) 1252 303 000
Lucent Technologies, Central America, Latin America	+1 408 324-3372 (USA)
Lucent Technologies, Asia Pacific 	+65 430 2100

(CFN 77115)