Avaya one-X® Mobile

Site Survey/Pre-Installation Checklist

Release 5.2

January 2010

0.2

00All Rights Reserved.

Notice

While reasonable efforts were made to ensure that the information in this document was complete and accurate at the time of printing, Avaya Inc. can assume no liability for any errors. Changes and corrections to the information in this document may be incorporated in future releases.

For full support information, please see the complete document, Avaya Support Notices for Software Documentation, document number 03-600758.

To locate this document on our Web site, simply go to http://www.avaya.com/support and search for the document number in the search box.

Documentation disclaimer

Avaya Inc. is not responsible for any modifications, additions, or deletions to the original published version of this documentation unless such modifications, additions, or deletions were performed by Avaya. Customer and/or End User agree to indemnify and hold harmless Avaya, Avaya's agents, servants and employees against all claims, lawsuits, demands and judgments arising out of, or in connection with, subsequent modifications, additions or deletions to this documentation to the extent made by the Customer or End User.

Link disclaimer

Avaya Inc. is not responsible for the contents or reliability of any linked Web sites referenced elsewhere within this documentation, and Avaya does not necessarily endorse the products, services, or information described or offered within them. We cannot guarantee that these links will work all of the time and we have no control over the availability of the linked pages.

Warranty

Avaya Inc. provides a limited warranty on this product. Refer to your sales agreement to establish the terms of the limited warranty. In addition, Avaya’s standard warranty language, as well as information regarding support for this product, while under warranty, is available through the following Web site:
http://www.avaya.com/support.

Copyright

Except where expressly stated otherwise, the Product is protected by copyright and other laws respecting proprietary rights. Unauthorized reproduction, transfer, and or use can be a criminal, as well as a civil, offense under the applicable law.

Cisco is a registered trademark of Cisco Systems, Inc.

Avaya support

Avaya provides a telephone number for you to use to report problems or to ask questions about your product. The support telephone number is 18002422121 in the United States. For additional support telephone numbers, see the Avaya Web site: http://www.avaya.com/support.

| [ 0 ] Company Contact Information |
| --- |
| 0.1 | Company Name: Address: Sold to #: |  |
| 0.2 | Main Contact / Project Manager: Email: Office Phone: Cell Phone: |  |
| 0.3 | Technical Contact: Email: Office Phone: Cell Phone: |  |

Review this and the tasks prior to the Avaya one-X® Mobile Server installation date.

| [ 1 ] Customer Tasks Basic INFO | Task Status / Notes |
| --- | --- |
| 1.0 | What version and release of Avaya Communication Manager do you wish to deploy with Avaya one-X Mobile? Latest version: 5.2, release 5.2.0.0.47 Minimum supported version 5.2 |  |
| 1.1 | What is the total number of users on your Avaya Communication Manager? |  |
| 1.2 | Are there multiple Avaya Communication Managers Networked? DCS +, QSIG What is Local and remote Ext. ranges… Identify each System and list the number of users separately. | Yes No |
| 1.3 | What hardware is hosting the Avaya Communication Manager where Avaya one-X Mobile is deployed? For example, Avaya S8800 1U server |  |
| 1.4 | How many users will use Avaya one-X Mobile? |  |
| 1.5 | Are the signaling group and the SIP trunk established on the Avaya Communication Manager? | Yes No Note: If No, then configure signaling group and SIP trunk. For more details, see the Avaya one-X® Mobile Integration, Administration and Maintenance Guide 142717. |
| 1.6 | Is the following SIP trunking information available? Note: If the answer is NO, please document this information. Available Trunk Group number in Communication Manager, Trunk group TAC code and COR, Available SIP Signaling group number, and CLAN or procr address and port for TCP/SIP signaling. | Yes NO |
| 1.7 | Are the Avaya one-X Mobile users configured for EC500 in Avaya Communication Manager? | Yes NO |
| 1.8 | Do you have additional PBX’s that are non Avaya Communication Managers networked? If yes, provide the following information: Type of PBX (e.g. Nortel etc.) How is the Avaya Communication Manager involved in the routing of calls to/from the other PBXs, if at all? | Yes NO |
| 1.9 | Does the Avaya Communication Manager has a DTMF software patch installed? (Dual Tone Multi Frequency functionality for interactive CTI operations) | Yes NO *Installed on License File* |
| 1.10 | How many digits are used in your internal dial plan for the 1XM users? |  |
| 1.11 | How is the outside line reached (For example, dial 9, *9)? |  |
| 1.12 | If a “1” is not required for 10-digit dialing of local numbers, provide a list of the NPA-NXXs for those numbers. |  |
| 1.13 | Do all users use the same dial plan(s) for outside lines? If not, explain how they differ |  |
| 1.14 | How many digits are passed on the T1/E1 circuit connected with your switch? |  |
| 1.15 | Do you use long distance authorization codes supplied by a carrier or external party? Does each user have a unique PIN? Does the user enter the PIN before or after the number is dialed? | “Not Supported” |
| 1.16 | Are forced authorization codes (FAC) and/or client matter codes (CMC) used on Avaya Communication Manager where Avaya one-X Mobile is deployed? For example, a FAC might be used to enable and disable a feature like call waiting; a CMC might be used to log minutes spent with a particular customer. | “Not Supported” |
| 1.17 | Provide information about the source, management, and use of any FACs and CMCs your system uses. For example: “Switch technician will configure call waiting on the Avaya Communication Manager. End users will dial *16 on their desk phone to enable call waiting and dial #16 to disable.” |  |
| 1.18 | Is Active Directory your Enterprise Directory Source? If not, what directory is used? |  |
| 1.19 | What version of Microsoft Active Directory do you use? If you use LDAP application other than Microsoft Active Directory, custom engineering may be required. |  |
| 1.20 | Is the Directory Authentication Source different from the Directory Look-up Source? If Different what is it? | Yes NO |
| 1.21 | Are there any other CTI applications that use JTAPI running on the Avaya Communication Manager? For example, call center applications used for individual agent monitoring. | Yes NO |
| 1.22 | If yes, are the same users that use Avaya one-X Mobile use these CTI applications? | Yes NO NA |
| 1.23 | Is the Avaya Communication Manager being used in a call center environment? | Yes NO |
| 1.24 | Is EC500 licensed and installed on the extensions on which Avaya one-X Mobile will be working? | Yes |
| 1.25 | Request EC500 set up. Provide user mobile number for the EC500. Note: Mapping mode = termination for EC500. | Provide a spread sheet that contains: First Name & Last Name DID that is in Active Directory under the telephone Number field. Extension in Communication Manager Cell # |
| 1.26 | What voicemail platform is used? What software version is used? What message store is used? If Microsoft Exchange is the message store, which version is used? For example: 2003, 2007, etc. Minimum supported version 2003 | Must be Modular Messaging |
| 1.27 | If Exchange is the message store, which version of Active Directory is used? |  |
| 1.28 | How many message store servers are in your network? |  |
| 1.29 | Are all your users that will be using Avaya one-X Mobile contained within the same message store database? | Yes No |
| [ 2 ] Customer Tasks Basic Setup | Task Status / Notes |
| 2.0 | Is this a single or split server deployment? See the Avaya one-X® Mobile Installation Guide, document number 18-602135, for information about single and split server configurations. | Single server residing in DMZ Single server internal network Single server internal w/reverse proxy Dual Server (Presentation) |
| 2.1 | Provide administrative user name and password for: Avaya Communication Manager super User Modular Messaging Trusted Server One X Mobile | Username Passwords Communication Manager: one-X Mobile: |
| 2.2 | Provide: Internal Edge IP address, External DMZ IP address (If used), Public Mapping IP to External (If used), URL for Public mapping DNS IP address, S87XX Active or Proc IP, MSS IP address, Clan IP Used for SAT (IP-Services) Ping connection from Avaya one-X Mobile internal server to PBX switch and MSS servers. If using DMZ ping from External to Internal. Note: The internal Avaya one-X Mobile Server should be on the same subnet as the Exchange server if using Exchange as your message store. SSH port 5022 & Telnet 5023 must be Enabled for Both Service State and Corp. LAN. | One-X Internal Edge IP : One-X External Edge IP (if used): One-X Public Mapping: URL for Public mapping: DNS IP Primary: DNS IP Secondary: DNS IP Tertiary: S87XX Active or Proc IP: MSS IP: Internal: Default GTWY: Subnet: DMZ: Default GTWY: Subnet: |
| 2.3 | Provide the following switch Feature Access Codes for input to Avaya one-X Mobile Admin Configuration: SAC Enable Code SAC Disable Code All users should have EC500 Appearance removed from their desk phone. Avaya one-X Mobile manages this through the application. |  |
| 2.4 | Provide the following information: LDAP User DN = (where login resides) Switch User Base DN = (where users) For example: cn=admin,ou=sales,cn=domain1,cn=users,dc=avaya,dc=com ou=sales,cn=domain1,cn=users,dc=avaya,dc=com | LDAP User DN: User Base DN: |
| 2.5 | Provide the following information: Microsoft Active Directory IP Administration Login Administrator password Note: Administrator must be able to read down with full permissions | AD IP or FQDN: Admin Login: Admin password: |
| 2.6 | Gather the following information Exchange Only: Microsoft Exchange username and password. Add user to the admin group of the local machine. | username password Exchange : Exchange user part of admin group on server? Yes NO |
| Access to Microsoft Exchange is required by the Avaya one-X Mobile Server to provide the Avaya one-X Mobile Visual Voicemail functionality. The Domain User is used by the Avaya one-X Mobile Application Suite to access voice messages from user mail boxes for this purpose. |
| 2.7 | Gather the following information: SMTP username SMTP password IP address IP port number Corporate email address Note: Person that wants to receive alerts | SMTP login/PWD if needed: SMTP server IP: SMTP port: 25 Admin Email address: |
| 2.8 | Provide a list of any Local NPA-NXXs that require 10-digit dialing without dialing a 1 to the dialed number. (Permissive Dialing). Note: Configuration is required. | List local NPA-NXXs: |
| 2.9 | List Carriers used for One-X Mobile Users’ NOTE: a Configuration set needed for Each Carrier | Carriers: Configuration Sets: |
| 2.10 | Verify that all potential users’ mobile devices are on the approved Avaya one- X® Mobile Certified Mobile Phone List. |  |
| 2.11 | Set up data plans and SMS with user’s wireless carrier. Note: It is recommended that users subscribe to an unlimited data plan and SMS messaging with 200 text messages per month. An example of a data plan is Cingular - Media Net. An example of an unlimited text messaging plan is Text/Instant Messaging 200.) | Data plans must be purchased through individual wireless carriers. |
| 2.12 | Provide all user names and their extensions. | Provide a spread sheet that contains: First Name & Last Name DID that is in Active Directory under the Telephone Number field. Extension in Communication Manager Cell # |
| 2.13 | Set up two test extensions for installation team testing. Support and submit IT request to add users. Then do the following: Establish extension in switch. Establish test users in Active Directory for authentication. Note: Avaya one-X Mobile administrative user must be able to authenticate to this organizational unit. | Test extension: First Name(sn=): Last Name(givenName): Handle/UserID(sAMAccountName): AD DID(telephoneNumber): EXT #: AD login name: AD PWD: MM PIN: |
| 2.14 | Schedule users for a 30- to 60-minute training session on the morning following Avaya one-X Mobile Server installation (provided by Customer). | Date: |
| [ 3 ] Avaya Tasks Communication Manager & Licensing | Task Status / Notes |
| 3.0 | Identify server racks for the Avaya one-X Mobile Server. Power Ethernet | Rack Location: Power: LAN: |
| 3.1 | Install Microsoft Windows Server 2003 (Standard or Enterprise edition) with Service Pack 2 or higher on the Avaya one-X Mobile Server and add Windows components of ASP.NET and IIS. Note: If the customer purchases the Avaya hardware/software from Avaya, it comes with Windows Server 2003 Standard Edition. If the customer purchases their own hardware, they can select Standard or Enterprise. Harden servers per corporate security standards. Apply SSL certificate on outside server as required by corporate security standards. Make sure the free space on the target drive is at least 6 GB and is not an even multiple of 4 GB. (This is a Microsoft Installer requirement.) | Windows version installed If Customer supplied Server: Service Pack: ASP.NET installed? IIS installed? SSL certificate installed? |
| 3.2 | Avaya one-X Mobile requires additional licensing for Avaya Communication Manager. This licensing is included in a material code when the product is ordered. Prior to configuring Avaya one-X Mobile, perform the following steps: Validate the following licenses exist: VALUE _SIP_TRK (Maximum Administered SIP Trunks) VALUE_PORT (Platform Maximum Ports) FEAT_EC500 (Enhanced EC500 = yes) VALUE_OPT_EC500 (Maximum Off-PBX Telephones = EC500) VALUE_OPT_PBFMC (Maximum Off-PBX Telephones = PBFMC) | Received Communication Manager licensing from Avaya? Is DTMF patch included? Filename: Filename: |

To create a domain user:

- In the Active Directory Users and Computer, create a domain user account in the domain where your Microsoft Exchange server resides.

NOTE:
If you have multiple Microsoft Exchange Servers, perform the following tasks on each Microsoft Exchange Server used by the Avaya one-X Mobile Application Suite.

- In the Microsoft Exchange System Manager, assign the permissions to Domain User as follows:

- Navigate to the Mailbox Store of the Microsoft Exchange Server.

- Right click Mailbox Store and select Properties.

- Select the Security tab.

- Click the Add button and add the Domain User.

- Assign the following permissions to the Domain User:

- Read

- Execute

- Delete

- Read permission

- Change permission

- List contents

- Read properties

- Write properties

- List object

- Open mail send queue

- Receive As

- Send As

- Once these permissions have been applied to the Domain User, stop and restart the Microsoft Exchange System Attendant Service, Microsoft Exchange MTA Stacks Service, and Microsoft Exchange Information Store Service. Optionally, you can wait for the update period to pass (usually around 24 hours) when the permissions assigned to the Domain User read into the Microsoft Exchange Applications.

The following firewall modifications are necessary for this topology: (From outside Network to DMZ/1XMobile server)

● Allow port 80 or 443 inbound traffic from any IP address to the Avaya one-X Mobile Server.

Note that it is problematic to restrict access-list entries to certain IP ranges for wireless networks as these networks are constantly changing their IP address ranges.

● Allow outbound traffic from the Avaya one-X Mobile Server to the Avaya Communication Manager/Cisco CallManager Cluster Nodes. The required ports are as follows:

- Port 80 for AXL needs to be opened to every Node in the Avaya Communication Manager/Cisco CallManager cluster.

- Port 2748 for JTAPI needs to be opened to every Node in the Cisco CallManager cluster.

- Port 450 needs to be open to AES for JTAPI communication.

Avaya one-X Mobile Server in the Same Network as other Servers (**Internal 1XM server**)

- Port 8404 for Avaya Communication Manager/Cisco CallManager LDAP needs to be opened to every Node in the Communication Manager/Cisco CallManager cluster.

- Port 389 for Microsoft Active Directory needs to be opened to the Active Directory Server.

- Port 143 for IMAP needs to be opened to the Microsoft Exchange Servers which home Avaya one-X Mobile users.

- Port 135 needs to be opened to the Microsoft Exchange Servers which home Avaya one-X Mobile users. This allows the MAPI protocol to access the Exchange Servers.

- Additionally, users in the inside network should be able to reach the DMZ via HTTP.

This is typically allowed by default on most firewalls.

Additional Info for Topology:

The following diagram illustrates a topology where the Avaya one-X Mobile Server functionality is split across two servers to keep only the parts necessary in the DMZ.

The Avaya one-X Mobile Server Handset Component can be homed in the DMZ with port 80/

443 access from the outside. The Avaya one-X Mobile Server is homed on the inside with LAN access to the Avaya Communication Manager and other servers it needs to communicate with. Communication between the DMZ and the inside is limited to Port 8080 (Tomcat) and port 1433 (ODBC).

Dual DMZ example:

Benefits of the Split Server Configuration

The Split Server configuration provides the following advantages:

- Incoming traffic from handsets can be easily load balanced in the DMZ.

- Access to port 80 and 443 is limited to the DMZ only.

- Firewall modifications to the inside interface is limited to 8080 and 1433.

- Critical Call Control functionality still resides on the inside next to the Avaya

- Communication Manager/Cisco CallManager. This is important in load situations.

- VPN software may be installed on the Mobile Handset Components.

In order to break into the network, a hacker would have to cross the following checkpoints:

- Outside firewall interface

- Avaya one-X Mobile handset component

- DMZ interface on port 8080 and port 1433

- Avaya one-X Mobile Server

| System Acceptance/Signoff |
| --- |
| Task | System Acceptance/Signoff | Task Completed By: | Date: |
|  | Validate that the test lines are functional and perform Avaya one-X Mobile basic set of tests including the following: Redirect calls to voicemail. Redirect calls to mobile device. Simulring. Redirect incoming call to office phone. Make a call back. Perform the following tests for the Avaya one-X Mobile Web application and mobile devices: Validate call logs show incoming calls. Validate call logs show outbound calls. Perform a corporate directory lookup. Initiate a call back via corporate directory lookup. Initiate a call back via personal directory lookup. Leave a voicemail for the test user. Check that the message shows up in the applications. Play the message from the applications. Save the test message. Delete the test message. |  |  |
|  | Set up for Avaya one-X Mobile Users |  |  |
|  | Have users download the Avaya one-X Mobile application on their mobile device and assist if necessary. |  |  |
|  | Train users on the Avaya one-X Mobile Web application. |  |  |
|  | Train users on the Avaya one-X Mobile application on their mobile device. |  |  |
|  | Verify message delivery, playback, and call redirection with a few users. |  |  |
|  | Access to Avaya one-X Mobile Server after Installation |  |  |
|  | Document how Avaya Support will access the Avaya one-X Mobile Server after initial implementation is completed. |  |  |
|  | Customer Installation Acceptance |  |  |
| 7 | Customer acknowledges Avaya one-X Mobile Service has been established and all users have been configured to their satisfaction. List any outstanding issues that may need to be addressed. NOTE: Provide customer with Avaya Support contact telephone number 1-800-242-2121. Customer Signature & Date: ________________________ Date: |  |  |